## Slide 1: Digital Design & Computer Arch. Lab 2 Supplement: Mapping Your Circuit to an FPGA
Prof. Onur Mutlu
ETH Zurich
Spring 2020
6 March 2020

## Slide 2: What Will We Learn?
In Lab 2, you will:
  Design a 4-bit adder.
    Design a 1-bit full-adder.
    Use full-adders to design a 4-bit adder.
  Learn how to map your circuits to an FPGA.
  Program your FPGA using the Vivado Design Suite for HDL design.
  Work with your FPGA board and see the results of your designs on the FPGA output.

## Slide 3: Binary Addition

## Slide 4: Binary Addition (1)
 |  | 0 | 1 | 1 | 1
+ |  | 1 | 0 | 1 | 0
A
B

## Slide 5: Binary Addition (2)
 |  |  | 1 |  | 
 |  | 0 | 1 | 1 | 1
+ |  | 1 | 0 | 1 | 0
 |  |  |  | 0 | 1
Carry

## Slide 6: Binary Addition (3)
 | 1 | 1 | 1 |  | 
 |  | 0 | 1 | 1 | 1
+ |  | 1 | 0 | 1 | 0
 | 1 | 0 | 0 | 0 | 1
A
B
Sum
Overflow
Carry

## Slide 7: The Full-Adder (1)
 | 1 | 1 | 1 |  | 
 |  | 0 | 1 | 1 | 1
+ |  | 1 | 0 | 1 | 0
 | 1 | 0 | 0 | 0 | 1

## Slide 8: The Full-Adder (2)
 | 1 | 1 | 1 |  | 
 |  | 0 | 1 | 1 | 1
+ |  | 1 | 0 | 1 | 0
 | 1 | 0 | 0 | 0 | 1
Inputs
Carry-in (Cin)
Input 1 (A)
Input 2 (B)
Outputs
Sum (S)
Carry-out (Cout)

## Slide 9: Design an Adder (1)
Design a full-adder:
  Inputs: input 1 (A), input 2 (B), carry-in (Cin).
  Outputs: sum (S), carry-out (Cout).
  All inputs and outputs are 1-bit wide.
Example:
  A = 1, B = 1, Cin = 1
  S = 1, Cout = 1
Full-adder
A
B
S
Cout
1-bit
1-bit
Cin
1-bit
1-bit
1-bit

## Slide 10: Design an Adder (2)
Design a 4-bit adder:
  Receives two 1-bit numbers A and B and a 1-bit input carry (Cin)
  Returns outputs S and C as sum and carry of the operation, respectively.
Example: A = 1110, B =0001, Cin=1
  S = 0000
  C = 1
Hint: Use four full-adders to design a 4-bit adder.

## Slide 11: Design an Adder (Overview)
You will use truth tables to derive the Boolean equation of the adder.
You will design the schematic of the circuit using logic gates.
You will use Vivado to write your design in Verilog.
You will use Vivado to program the FPGA.

## Slide 12: Vivado Design Suite
We will use the Vivado Design Suite for FPGA programming.
  Vivado is installed in the computers in the lab rooms.
  If you wish to use your own computer, you can follow these instructions:
  https://reference.digilentinc.com/learn/programmable-logic/tutorials/basys-3-getting-started/start

## Slide 13: Verilog

## Slide 14: Defining a Module in Verilog
A module is the main building block in Verilog.
We first need to define:
  Name of the module
  Directions of its ports (e.g., input, output)
  Names of its ports
Then:
  Describe the functionality of the module.
inputs
output
example

## Slide 15: Implementing a Module in Verilog
module example (a, b, c, y);
input a;
input b;
input c;
output y;
// here comes the circuit description
endmodule
Port list
(inputs and outputs)
ports have a declared type
a module definition
name of module
example

## Slide 16: Structural HDL: Instantiating a Module
Schematic of module “top” that is built from two instances of module “small”
i_first
i_second
Notes: TODO: make I consistent

## Slide 17: Structural HDL Example (1)
Module Definitions in Verilog
module small (A, B, Y);
input A;
input B;
output Y;
// description of small
endmodule
i_first
i_second

## Slide 18: Structural HDL Example (2)
Module Definitions in Verilog
module top (A, SEL, C, Y);
input A, SEL, C;
output Y;
wire n1;
endmodule
module small (A, B, Y);
input A;
input B;
output Y;
// description of small
endmodule
i_first
i_second

## Slide 19: Structural HDL Example (3)
module top (A, SEL, C, Y);
input A, SEL, C;
output Y;
wire n1;
endmodule
module small (A, B, Y);
input A;
input B;
output Y;
// description of small
endmodule
Defining wires (module interconnections)
i_first
i_second

## Slide 20: Structural HDL Example (4)
The first instantiation of the “small” module
module top (A, SEL, C, Y);
input A, SEL, C;
output Y;
wire n1;
// instantiate small once
small i_first ( .A(A),
.B(SEL),
.Y(n1) );
endmodule
module small (A, B, Y);
input A;
input B;
output Y;
// description of small
endmodule
i_first
i_second

## Slide 21: Structural HDL Example (5)
The second instantiation of the “small” module
module top (A, SEL, C, Y);
input A, SEL, C;
output Y;
wire n1;
// instantiate small once
small i_first ( .A(A),
.B(SEL),
.Y(n1) );
// instantiate small second time
small i_second ( .A(n1),
.B(C),
.Y(Y) );
endmodule
module small (A, B, Y);
input A;
input B;
output Y;
// description of small
endmodule
i_first
i_second

## Slide 22: Structural HDL Example (6)
Short form of module instantiation
module top (A, SEL, C, Y);
input A, SEL, C;
output Y;
wire n1;
// alternative
small i_first ( A, SEL, n1 );
/* Shorter instantiation,
pin order very important */
// any pin order, safer choice
small i_second ( .B(C),
.Y(Y),
.A(n1) );
endmodule
module small (A, B, Y);
input A;
input B;
output Y;
// description of small
endmodule
i_first
i_second

## Slide 23: What about logic gates?

## Slide 24: Instantiating Logic Gates: The NOT Gate
not my_not(output, input);
gate type
gate name
output signal
input signal
input
output
0 | 1
1 | 0
0 | 1
1 | 0

## Slide 25: Instantiating Logic Gates: The AND Gate (1)
and my_and(output, input1, input2);
gate type
gate name
output signal
input signals
A
B
A · B
 |  | •
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 26: Instantiating Logic Gates: The AND Gate (2)
and my_and(output, input1, input2);
or…
and my_and(output, input1, input2, input3, ...);
gate type
gate name
output signal
input signals (as many as you want)
gate type
gate name
output signal
input signals
A
B
A · B
 |  | •
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 27: Instantiating Logic Gates: More Gates…
not my_not(output, input);
and my_and(output, input1, input2, ...),
or my_or(output, input1, input2, ...);
xor my_xor(output, input1, input2, ...);
nand my_nand(output, input1, input2, ...);
nor my_nor(output, input1, input2, ...);
xnor my_xnor(output, input1, input2, ...);

## Slide 28: Instantiating Logic Gates: A Simple Example (1)

## Slide 29: Instantiating Logic Gates: A Simple Example (2)
// Notice the alternative port declaration
module check_zeros (
input A,
input B,
output out
);
// wires for the intermediate signals
wire not_a, not_b;
// instantiate the NOT gates
not(not_a, A);
not(not_b, B);
// instantiate the AND gate
and(out, not_a, not_b);
endmodule

## Slide 30: Basys 3 FPGA Board
In this course, we will be using the Basys 3 boards from Digilent, as shown below.
You can learn more about the Basys 3 Starter Board from:
http://store.digilentinc.com/basys-3-artix-7-fpga-trainer-board-recommended-for-introductory-users/
Output LEDs
Input Switches
For this week’s lab:

## Slide 31: Last Words
In this lab, you will map your circuit to an FPGA.
First you will design a full-adder. You will then use the full-adder as a building block to build a 4-bit adder.
Then, you will learn how to use Xilinx Vivado for writing Verilog and how to connect to the Basys 3 board.
Finally, you will program the FPGA and get the circuit running on the FPGA board.
You will find more exercises in the lab report.

## Slide 32: Report Deadline
23:59, 27 March 2020

## Slide 33: Digital Design & Computer Arch. Lab 2 Supplement: Mapping Your Circuit to an FPGA
Prof. Onur Mutlu
ETH Zurich
Spring 2020
6 March 2020